APPENDIX 3

Practice Summary Guide for Pesticide Losses

| Practice | Pesticide Loss Pathways | Comments |
| --- | --- | --- |
|  | Leaching | Adsorption | Runoff |  |
| Management Practices 1/ |  |  |  |  |
| Lower Application Rate | +++ | ++ | ++ | Most effective with highly soluble pesticides |
| Partial Substitution | +++ | ++ | ++ | Use pesticides with lower environmental risk |
| Partial Treatment | ++ | +++ | +++ | Banding and directed spraying, most effective with strongly adsorbed pesticides |
| Formulation | +++ | + | + | Less soluble pesticides move slower |
| Erodibility, Runoff, Leaching | +++ | ++ | ++ | Follow special label restrictions where pesticides will be applied to soils which are subject to erosion, runoff, or leaching |
| Soil Incorporation | ++ | ++ | ++ | Reduces amount of pesticides at the soil surface, reduces macropore flow |
| Application Timing | +++ | +++ | +++ | Pesticide losses decrease with time between application and storm events |
| Set-back | ++ | ++ | ++ | Greater distance from surface water and less inadvertent application to water body, greater distance to entry point |
| Conservation Practices 2/ |  |  |  |  |
| Conservation Cover (327) | +++ | +++ | +++ | For use when land is retired from production |
| Conservation Crop Rotation (328) | ++ | +++ | +++ | Pesticide use can be reduced due to rotational effects on pest complex |
| Contour Buffer Strips (332) | + | +++ | ++ | Reduces runoff. Sediment deposited above buffer. |
| Contour Farming (330) |  | + | + | Infiltration improved, runoff reduced |
| Cover Crop (340) | + | ++ | + | Reduces transport of adsorbed pesticides |
| Deep Tillage (324) | - | + | + | Shattering of restrictive layers reduces runoff and sedimentation and sedimentation |
| Field Border (386) |  | +++ | ++ | Buffer action reduces runoff and suspended sediment |
| Filter Strip (393) | + | +++ | ++ | Reduces runoff, sediment deposited above filter strip |
| Grade Stabilization Structure (410) |  | +++ |  | Reduces mass movement of soil and adsorbed pesticides |
| Grassed Waterway (412) | + | ++ | + | Some trapping of adsorbed pesticides |
| Irrigation Land Leveling (464) | + | ++ |  | Reduction of suspended sediment and transport of adsorbed pesticides |
| Irrigation System Tail Water Recovery (447) | - | ++ | ++ | Reductions in runoff and suspended sediment |
| Irrigation Water Management (449) | ++ | + | + | Reductions in runoff and suspended sediment |
| Pasture and Hay Planting (512) | ++ | +++ | +++ | Rotation including perennial grasses and legumes generally require fewer pesticides |
| Prescribed Grazing (528A) |  | +++ | ++ | Proper management of grazing and browsing animals improves plant health reducing the need for pesticides |
| Residue Management, No-Till (329A) |  | ++ | ++ | Significant reduction in adsorbed and highly soluble pesticide leaving a field |
| Residue Management, Mulch-Till (329B) |  | +++ | ++ | Significant reduction in adsorbed and highly soluble pesticide leaving a field |
| Residue Management, Ridge Till (329C) |  | +++ | ++ | Significant reduction in adsorbed and highly soluble pesticide leaving a field |

APPENDIX THREE – Practice Summary Guide for Pesticide Losses (Continued)

| Practice | Pesticide Loss Pathways | Comments |
| --- | --- | --- |
|  | Leaching | Adsorption | Runoff |  |
| Management Practices 1/ |  |  |  |  |
| Residue Management, Seasonal (344) |  | ++ | + | Slight to moderate reductions in adsorbed and highly soluble pesticides leaving a field |
| Riparian Forest Buffer (391) | + | +++ | +++ | Slight to significant reduction in pesticide contamination of shallow ground water and surface water |
| Terrace (600) | - | +++ | ++ | Moderate to significant reductions of runoff and suspended sediment carrying soluble or adsorbed pesticides |
| Tree and Shrub Establishment (612) | ++ | +++ | +++ | Moderate to significant reductions in pesticide usage |
| Waste Storage Facility (313) | + | ++ | ++ | Wastes containing pesticide residues are properly contained and not exposed to environmental element |
| Waste Treatment Lagoon (359) |  | +++ | +++ | Pesticides in runoff and adsorbed to suspended sediment are captured and degraded |
| Waste Utilization | + | ++ | + | Increased microbial degradation of pesticide residues |
| Well Decommissioning (351) | +++ |  |  | Closure of entry points of pesticides into ground water |
| Wetland Wildlife Habitat Management (644) | ++ | ++ | ++ | Filtering and degradation of pesticides entering wetland environments |

1/  Additional information on management practices can be obtained from the Field Office

Technical Guide, NRCS personnel, Texas Cooperative Extension Service and pesticide

labels.

2/ Details regarding the effects of conservation practices on surface and ground water

contamination by pesticides are contained in the Conservation Practice Physical Effects

found in the Field Office Technical Guide.