Natural Resources Conservation Service

Conservation Practice Standard

Pest Management

(Acre)

Code 595

# Definition

Utilizing environmentally sensitive prevention, avoidance, monitoring and suppression strategies, to manage weeds, insects, diseases, animals and other organisms (including invasive and non-invasive species), that directly or indirectly cause damage or annoyance.

# Purposes

This practice is applied as part of a Resource Management System (RMS) to support one or more of the following purposes:

- Enhance quantity and quality of commodities.

- Minimize negative impacts of pest control on soil resources, water resources, air resources, plant resources, animal resources and/or humans.

# Conditions Where Practice Applies

Wherever pests will be managed.

CRITERIA

## General Criteria Applicable to All Purposes

A pest management component of a conservation plan shall be developed that meets the Resource Management System (RMS) level of quality criteria in the local FOTG.

All methods of pest management must comply with Federal, Tribal, State, and local regulations, including management plans for invasive pest species, noxious weeds and disease vectors. Compliance with the Food Quality Protection Act (FQPA); Federal Insecticide, Fungicide and Rodenticide Act (FIFRA); Worker Protection Standard (WPS); and Interim Endangered Species Protection Program (H7506C) is required for chemical pest control.

Persons who approve plans for pest management shall be certified through a program acceptable to NRCS within the state.

Where used, the client and/or their representative will provide pesticide recommendations for the pest management component of the conservation plan.

Integrated Pest Management (IPM) that strives to balance economics, efficacy and environmental risk, where available, shall be incorporated into planning alternatives.

IPM is a sustainable approach to pest control that combines the use of prevention, avoidance, monitoring and suppression strategies, to maintain pest populations below economically damaging levels, to minimize pest resistance, and to minimize harmful effects of pest control on human health and environmental resources. IPM suppression systems include biological controls, cultural controls and the judicious use of chemical controls.

Crop specific IPM recommendations for planning alternatives are available from the University of Idaho, Oregon State University and Washington State University sources:

- Pacific Northwest Pest Management Coalition, http://ippc.orst.edu/IPM-NW-ecoregion/index.cfm.

- University of Idaho Pest Management Center, http://www.ag.uidaho.edu/pmc/.

- Integrated Plant Protection Center, http://www.ippc.orst.edu/.

- Washington State Pest Management Resource Service, http://wsprs.wsu.edu/.

Where crop specific IPM recommendations are not available, the IPM principles listed in the consideration section (page 4) of this standard shall be utilized to develop pest management alternatives.

An appropriate set of mitigation techniques must be planned and implemented to reduce the environmental risks of pest management activities in accordance with quality criteria in the local Field Office Technical Guide. Mitigation techniques include practices like a Filter Strip or Conservation Crop Rotation, and management techniques like application method or timing.

All methods of pest management must be integrated with other components of the conservation plan.

Clients shall be instructed to pay special attention to all environmental hazards and site-specific application criteria listed on pesticide labels and contained in Extension and Crop Consultant recommendations.

## Additional Criteria to Protect Quantity and Quality of Commodities

As an essential component of both commodity-specific IPM and IPM general principles, clients shall be encouraged to use the minimum level of pest control necessary to meet their objectives for commodity quantity and quality.

## Additional Criteria to Protect Soil Resources

In conjunction with other conservation practices, the number, sequence and timing of tillage operations shall be managed to maintain soil quality and maintain soil loss at or below the soil loss tolerance (T) or any other planned soil loss objective.

The current approved erosion prediction technology for wind and water and the current approved soil condition index procedure shall be used.

Clients shall be encouraged to pay special attention to pesticide label instructions for limiting pesticide residues in soil that may negatively impact non-target plants, animals and humans.

## Additional Criteria to Protect Water Resources

Pest management environmental risks, including the impacts of pesticides in ground and surface water on humans and non-target plants and animals, must be evaluated for all identified water resource concerns.

Evaluations shall be made using the current version of the Windows Pesticide Screening Tool (WIN-PST) available at, http://www.wcc.nrcs.usda.gov/water/quality/frame/pestmgt.html.

When a chosen alternative has the potential to negatively impact important water resources, (e.g., WIN-PST “Extra High”, “High” or “Intermediate” soil/pesticide human risk ratings in the drainage area of a drinking water reservoir or WIN-PST “Extra High, “High” or “Intermediate” soil/pesticide fish risk ratings in a drainage area providing habitat for resident and/or anadromous fish), an appropriate set of mitigation techniques must be put in place to address risks to humans and non-target plants and animals.

Table 1 – Oregon Mitigation Effectiveness Guide to Reduce Pesticide Impacts on Surface and Ground Water shall be used to mitigate impacts of the pest management alternatives selected by the client.

Clients shall be encouraged to pay special attention to pesticide label instructions for limiting pesticide residues in leachate and runoff that may negatively impact non-target plants, animals and humans.

The number, sequence and timing of tillage operations shall be managed in conjunction with other sediment control tactics and practices, in order to minimize sediment losses to nearby surface water bodies.

## Additional Criteria to Protect Air Resources

Clients shall be encouraged to pay special attention to pesticide label instructions for minimizing volatilization and drift that may negatively impact non-target plants, animals and humans.

## Additional Criteria to Protect Plant Resources

Clients shall be encouraged to pay special attention to pesticide label instructions including those directed at:

- Preventing misdirected pest management control measures that negatively impact plants (e.g., removing pesticide residues from sprayers before moving to the next crop and properly adjusting cultivator teeth and flame burners).

- Appropriate climatic conditions, crop stage, soil moisture, pH, and organic matter in order to protect plant health.

- Limiting pesticide residues in soil that can carry over and harm subsequent crops.

## Additional Criteria to Protect Animal Resources

Clients shall be encouraged to pay special attention to pesticide label instructions that minimize negative impacts to animals.

## Additional Criteria to Protect Humans

Clients shall be encouraged to pay special attention to pesticide label instructions that minimize negative impacts to humans.

# Considerations

If commodity-specific IPM is not available, the following IPM principles should be considered:

- Prevention, such as using pest-free seeds and transplants, cleaning tillage and harvesting equipment between fields, irrigation scheduling to avoid situations conducive to disease development, etc.

- Avoidance, such as using pest resistant varieties, crop rotation, trap crops, etc.

- Monitoring, such as pest scouting, soil testing, weather forecasting, etc. to help target suppression strategies and avoid routine preventative pest control.

- Suppression, such as cultural, biological and chemical controls, that can reduce a pest population or its impacts. Chemical controls should be used judiciously in order to minimize environmental risk and pest resistance.

Adequate plant nutrients and soil moisture, including favorable pH and soil conditions, should be available to reduce plant stress, improve plant vigor and increase the plant's overall ability to tolerate pests.

On irrigated land, irrigation water management should be designed to minimize pest management environmental risk.

# PLANS AND SPECIFICATIONS

The pest management component of a conservation plan shall be prepared in accordance with the criteria of this standard using the Pest Management Specification Sheet, 595 OR-Specification and shall describe the requirements for applying the practice to achieve its intended purpose(s).

As a minimum, the pest management component of a conservation plan shall include:

- Plan map and soil map of managed site, if applicable (use RMS plan maps if available).

- Location of sensitive resources and setbacks, if applicable (use RMS plan maps if available).

- Environmental risk analysis, with approved tools and/or procedures, for probable pest management recommendations by crop (if applicable) and pest.

- Interpretation of the environmental risk analysis and identification of appropriate mitigation techniques.

- Operation and maintenance requirements.

# Operation and Maintenance

The pest management component of a conservation plan shall include appropriate operation and maintenance items for the client. These may include:

- Review and update the plan periodically in order to incorporate new IPM technology, respond to cropping system and pest complex changes, and avoid the development of pest resistance.

- Maintain mitigation techniques identified in the plan in order to ensure continued effectiveness.

- Develop a safety plan for individuals exposed to chemicals, including telephone numbers and addresses of emergency treatment centers for individuals exposed to chemicals and the telephone number for the nearest poison control center. The National Pesticide Information Center (NIPC) telephone number in Corvallis, Oregon may also be given for non-emergency information:

1-800-858-7378

Monday - Friday

6:30 a.m. to 4:30 p.m. Pacific Time

For advice and assistance with emergency spills that involve agrichemicals, the local emergency telephone number should be provided.

The national 24-hour CHEMTREC telephone number may also be given:

1-800-424-9300

- Follow label requirements for mixing/loading setbacks from wells, intermittent streams and rivers, natural or impounded ponds and lakes, or reservoirs. (State or local regulations may be more restrictive).

- Post signs according to label directions and/or Federal, State, and local laws around sites that have been treated. Follow restricted entry intervals.

- Dispose of pesticides and pesticide containers in accordance with label directions and adhere to Federal, State, and local regulations.

- Read and follow label directions and maintain appropriate Material Safety Data Sheets (MSDS).

- Calibrate application equipment according to Extension and/or manufacturer recommendations before each seasonal use and with each major chemical change.

- Replace worn nozzle tips, cracked hoses, and faulty gauges.

- Maintain records of pest management for at least two years. Pesticide application records shall be in accordance with USDA Agricultural Marketing Service's Pesticide Record Keeping Program.

- Report annual pesticide use as per Oregon Pesticide Use Reporting System (PURS) requirements.  PURS information is available at, http://oda.state.or.us/purs/.

Table 1

Oregon Mitigation Effectiveness Guide

To Reduce Pesticide Impacts on Surface and Ground Water

Pest Management (595) requires environmental risks evaluation and appropriate mitigation for all identified resource concerns. This table identifies management techniques, many which are IPM techniques and conservation practices that have the potential to mitigate pesticide impacts on water quality. Not all techniques will be applicable to a given situation. Relative effectiveness ratings by pesticide loss pathway are “no effect” (blank), “slight effect” (+/-), “moderate effect” (++/--), and “significant effect” (+++/---). The table also identifies how the techniques function. Effectiveness of any mitigation technique can be highly variable based on site conditions, and how it is designed. Therefore, with guidance provided by the table, site-specific selection and design of mitigation techniques that are appropriate for identified resource concerns is left to the professional judgment of the conservation planner.

| Pest Management Mitigation Techniques | Pesticide Loss Pathways | Function |
| --- | --- | --- |
|  | Leaching | Solution Runoff | Adsorbed Runoff |  |
| Management Techniques 1/ |  |  |  |  |
| Application Timing | +++ | +++ | +++ | Reduces exposure potential – delaying application when significant rainfall events are forecast can reduce pesticide transport to ground and surface water, application when conditions are optimal can reduce the amount of pesticide applied, also delaying application when wind speed is not in accordance with label requirements can reduce pesticide drift to surface water |
| Formulations/ Adjuvants | ++ | ++ | + | Reduces exposure potential – formulations and/or adjuvants that increase efficacy allow lower application rates |
| Lower Application Rates | +++ | +++ | +++ | Reduces exposure potential – use lowest effective rate |
| Partial Treatment | +++ | +++ | +++ | Reduces exposure potential – spot treatment, banding and directed spraying reduce amount of pesticide applied |
| Pesticide Label Environmental Hazard Warnings and BMPs | Required 2/ | Required2/ | Required 2/ | Reduces exposure potential – label guidance must be carefully followed for pesticide applications near water bodies and on soils that are intrinsically vulnerable to erosion, runoff, or leaching |
| Scouting and Integrated Pest Management (IPM)Thresholds | +++ | +++ | +++ | Reduces exposure potential – reduces the amount of pesticide applied |
| Set-backs | + | ++ | + | Reduces exposure potential – reduced application area reduces amount of pesticide applied, can also reduce inadvertent pesticide application and drift to surface water |
| Soil Incorporation – mechanical or irrigation | --- | +++ | +++ | Reduces exposure potential for surface losses, but increases exposure potential for leaching losses |
| Substitution – Alternative pesticides Cultural controls Biological controls | +++ | +++ | +++ | Reduces hazard potential - use alternative pesticides with low environmental risk, substituting cultural (including burning and mechanical controls) and biological controls can reduce the need for pesticides |

| Mitigation Technique | Pesticide Loss Pathways | Function |
| --- | --- | --- |
|  | Leaching | Solution Runoff | Adsorbed Runoff |  |
| Conservation Practices 3/ |  |  |  |  |
| Agrichemical Mixing Center (Interim 702) | +++ | +++ | +++ | Reduces the potential for point source pesticide contamination |
| Alley Cropping (311) | + | + | ++ | Increases infiltration and uptake of subsurface water, reduces soil erosion, can provide habitat for beneficial insects which can reduce the need for pesticides, also can reduce pesticide drift to surface water |
| Anionic Polyacrylamide (PAM) Erosion Control (450) | - | + | +++ | Increases infiltration and deep percolation, reduces soil erosion |
| Bedding (310) | + | + | + | Increases surface infiltration and aerobic pesticide degradation in the rootzone |
| Brush Management (314) | +++ | +++ | +++ | Using non-chemical brush control often reduces the need for pesticides, pesticide use requires environmental risk analysis and appropriate mitigation – see Pest Management (595) |
| Conservation Cover (327) | +++ | +++ | +++ | Retiring land from annual crop production often reduces the need for pesticides, builds soil organic matter |
| Constructed Wetland (656) | + | + | ++ | Captures pesticide residues and facilitates their degradation |
| Conservation Crop Rotation (328) | ++ | ++ | ++ | Reduces the need for pesticides by breaking pest lifecycles |
| Contour Buffer Strips (332) |  | ++ | ++ | Increases infiltration, reduces soil erosion |
| Contour Farming (330) | - | + | + | Increases infiltration and deep percolation, reduces soil erosion |
| Contour Orchard and Other Fruit Area (Ac.) (331) | - | + | + | Increases infiltration and deep percolation, reduces soil erosion |
| Stripcropping (585) |  | ++ | ++ | Increases infiltration, reduces soil erosion |
| Cover Crop (340) | + | + | ++ | Increases infiltration, reduces soil erosion, builds soil organic matter |
| Cross Wind Ridges (589A) |  |  | (+) 4/ | Reduces wind erosion and adsorbed pesticide deposition in surface water |
| Cross Wind Stripcropping (589B) |  |  | (++) 4/ | Reduces wind erosion and adsorbed pesticide deposition in surface water, traps adsorbed pesticides |
| Cross Wind Trap Strips (589C) |  |  | (++) 4/ | Reduces wind erosion and adsorbed pesticide deposition in surface water, traps adsorbed pesticides |
| Deep Tillage (324) | - | + | + | Increases infiltration and deep percolation |
| Dike (356) | ++/-- | ++ | ++ | Reduces exposure potential – excludes outside water (++ leaching) or captures pesticide residues and facilitates their degradation (-- leaching) |
| Diversion (362) | + | + | + | Reduces exposure potential – water is diverted |
| Drainage Water Management (554) | ++/-- | ++ | ++ | Seasonal saturation may reduce the need for pesticides, drainage reduces storm water runoff, drainage increases infiltration and aerobic pesticide degradation in the rootzone during the growing season (++ leaching), seasonal saturation may bring the water table in contact with pesticide residues from the previous growing season (-- leaching) |
| Field Border (386) |  | + | ++ | Increases infiltration and traps adsorbed pesticides, often reduces application area resulting in less pesticide applied, can provide habitat for beneficial insects which reduces the need for pesticides, can provide habitat to congregate pests which can result in reduced pesticide application, also can reduce inadvertent pesticide application and drift to surface water |
| Filter Strip (393) |  | ++ | +++ | Increases infiltration and traps adsorbed pesticides, often reduces application area resulting in less pesticide applied, can provide habitat for beneficial insects which reduces the need for pesticides, can provide habitat to congregate pests which can result in reduced pesticide application, also can reduce inadvertent pesticide application and drift to surface water |
| Floodwater Diversion (400) | + | + | + | Reduces exposure potential – floodwater is diverted |
| Forage Harvest Management (511) | ++ | ++ | ++ | Reduces exposure potential – timely harvesting reduces the need for pesticides |
| Forest Stand Improvement (666) | ++ | ++ | ++ | Reduces the potential for pest damage and the need for pesticides |
| Grade Stabilization Structure (410) |  |  | ++ | Traps adsorbed pesticides |
| Grassed Waterway (412) |  | + | ++ | Increases infiltration and traps adsorbed pesticides (should be applied with Filter Strips at the outlet and on each side of the waterway) |
| Grazing Land Mechanical Treatment (548) | - | + | + | Increases infiltration and deep percolation |
| Hedgerow Planting (442) |  |  | (+) 4/ | Reduces adsorbed pesticide deposition in surface water, also can reduce inadvertent pesticide application and drift to surface water |
| Herbaceous Wind Barriers (603) |  |  | (+) 4/ | Reduces wind erosion, traps adsorbed pesticides, can provide habitat for beneficial insects which reduces the need for pesticides, can provide habitat to congregate pests which can result in reduced pesticide application, also can reduce pesticide drift to surface water |
| Hillside Ditch (423) | + | + | + | Reduces exposure potential – water is diverted |
| Irrigation Land Leveling (464) | ++ | + | ++ | Reduces exposure potential – uniform surface reduces pesticide transport to ground and surface water |
| Irrigation System, Microirrigation (441) | ++ | +++ | +++ | Reduces exposure potential – efficient and uniform irrigation reduces pesticide transport to ground and surface water |
| Irrigation System, Sprinkler (442) | ++ | ++ | ++ | Reduces exposure potential – efficient and uniform irrigation reduces pesticide transport to ground and surface water |
| Irrigation System, Surface and Subsurface (443) | + | + | + | Reduces exposure potential – efficient and uniform irrigation reduces pesticide transport to ground and surface water |
| Irrigation System Tail Water Recovery (447) |  | +++ | +++ | Captures pesticide residues and facilitates their degradation |
| Irrigation Water Management (449) | +++ | +++ | +++ | Reduces exposure potential – water is applied at rates that minimize pesticide transport to ground and surface water, promotes healthy plants which can better tolerate pests |
| Land Smoothing (466) | + | + | + | Reduces exposure potential – uniform surface reduces pesticide transport to ground and surface water |
| Mole Drain (482) | + | + | + | Increases infiltration and aerobic pesticide degradation in the rootzone *Note – avoid direct outlets to surface water |
| Mulching (484) | + | +/- | +/- | Often reduces the need for pesticides, natural mulches increase infiltration and reduce soil erosion (+ solution and adsorbed runoff), artificial mulches may increase runoff and erosion (- solution and adsorbed runoff) |
| Nutrient Management (590) | ++ | ++ | ++ | Promotes healthy plants which can better tolerate pests |
| Pasture and Hay Planting (512) | ++ | ++ | ++ | Retiring land from annual crop production often reduces the need for pesticides, builds soil organic matter |
| Precision Land Forming (462) | ++ | + | ++ | Reduces exposure potential – uniform surface reduces pesticide transport to ground and surface water |
| Prescribed Burning (338) | ++ | ++ | ++ | Often reduces the need for pesticides |
| Prescribed Grazing (528A) | ++ | ++ | ++ | Improves plant health and reduces the need for pesticides |
| Range Planting (550) | ++ | ++ | ++ | Increases infiltration and uptake of subsurface water, reduces soil erosion, builds soil organic matter |
| Recreation Area Improvement (562) | ++ | ++ | ++ | Increases infiltration and uptake of subsurface water, reduces soil erosion, builds soil organic matter |
| Residue Management, Direct Seed (777) | + | ++ | +++ | Increases infiltration, reduces soil erosion, builds soil organic matter |
| Residue Management, No-till and Strip-Till (329A) | + | ++ | +++ | Increases infiltration, reduces soil erosion, builds soil organic matter |
| Residue Management, Mulch-Till (329B) | + | ++ | +++ | Increases infiltration, reduces soil erosion, builds soil organic matter |
| Residue Management, Ridge Till (329C) | + | ++ | +++ | Increases infiltration, reduces soil erosion, builds soil organic matter |
| Residue Management, Seasonal (344) | + | ++ | ++ | Increases infiltration, reduces soil erosion, builds soil organic matter |
| Riparian Forest Buffer (391) | + | +++ | +++ | Increases infiltration and uptake of subsurface water, traps sediment, builds soil organic matter |
| Riparian Herbaceous Cover (390) | + | ++ | ++ | Increases infiltration, traps sediment, builds soil organic matter |
| Row Arrangement (557) | - | + | + | Increases infiltration and deep percolation, reduces soil erosion |
| Sediment Basin (350) |  |  | ++ | Captures pesticide residues and facilitates their degradation |
| Stripcropping, Field (586) |  | + | + | Increases infiltration, reduces soil erosion |
| Structure For Water Control (587) | - | ++ | +++ | Captures pesticide residues and facilitates their degradation, increases infiltration and deep percolation |
| Subsurface Drainage (606) | + | ++ | ++ | Increases infiltration and aerobic pesticide degradation in the rootzone *Note – avoid direct outlets to surface water |
| Surface Drainage, Field Ditch (607) | + | + | + | Increases infiltration and aerobic pesticide degradation in the rootzone |
| Surface Roughening (609) |  |  | (+) 4/ | Reduces wind erosion and adsorbed pesticide deposition in surface water |
| Terrace (600) | -- | ++ | +++ | Increases infiltration and deep percolation, reduces soil erosion |
| Tree and Shrub Establishment (612) | +++ | +++ | +++ | Retiring land from annual crop production often reduces the need for pesticides, increases infiltration and uptake of subsurface water, builds soil organic matter |
| Vegetative Barriers (601) |  |  | ++ | Reduces soil erosion, traps sediment, increases infiltration |
| Waste Storage Facility (313) | + | ++ | ++ | Captures pesticide residues |
| Waste Treatment Lagoon (359) |  | +++ | +++ | Captures pesticide residues and facilitates their degradation |
| Waste Utilization (633) | ++ | ++ | ++ | Increases soil organic matter |
| Water and Sediment Control Basin (638) | - | ++ | +++ | Captures pesticide residues and facilitates their degradation, increases infiltration and deep percolation |
| Waterspreading (640) | - | + | + | Increases infiltration and deep percolation |
| Well Decommissioning (351) | +++ |  |  | Eliminates point source contamination |
| Wetland Creation (Ac.) (658) | + | + | + | Captures pesticide residues and facilitates their degradation |
| Wetland Enhancement (Ac.) (659) | + | + | + | Captures pesticide residues and facilitates their degradation |
| Wetland Restoration (Ac.) (657) | + | + | + | Captures pesticide residues and facilitates their degradation |
| Windbreak/Shelterbelt Establishment (380) |  |  | (++) 4/ | Reduces wind erosion, reduces adsorbed pesticide deposition in surface water, traps adsorbed pesticides, also can reduce pesticide drift |
| Windbreak/Shelterbelt Renovation (650) |  |  | (++) 4/ | Reduces wind erosion, reduces adsorbed pesticide deposition in surface water, traps adsorbed pesticides, also can reduce pesticide drift |

1/ Additional information on pest management mitigation techniques can be obtained from Extension pest management publications, pest management consultants and pesticide labels.

2/ The pesticide label is the law - all pesticide label specifications must be carefully followed, including required mitigation.
    Additional mitigation may be needed to meet NRCS pest management requirements for identified resource concerns.

3/ Details regarding the effects of Conservation Practices on ground and surface water contamination by pesticides are contained in the Conservation Practice Physical Effects matrix found in the National Handbook of Conservation Practices.

4/ Mitigation applies to adsorbed pesticide losses being carried to surface water by wind.